## Slide 1
Mapping the Wild in 3D: LiDAR Insights into Forest Ecology
Fei Zhang1, Rob Chancia1, Richard MacKenzie2, Jan van Aardt1
1
2
Introduction
  Forests are full of complex structures that shape biodiversity and ecosystem health. Using terrestrial LiDAR, we capture detailed 3D scans of two distinct environments: the temperate woodlands of Harvard Forest and the tangled mangrove forest of Palau. These 3D point clouds reveal patterns in vegetation that support research in ecology, conservation, and environmental monitoring.
Scanning the Wild: Sites, LiDAR, and 3D Data
Semi-Automated LiDAR Annotation
Faster, smarter, accurate, and scalable
Results, Highlights & Future Work
Wavelength | 905 nm
Max range | 50 m
Range error | 30 mm
Beam divergence | 0.86°
Angular resolution | 0.25°
Angular coverage | 360° × 270°
Scan duration | 33 s
Mass | 3.9 kg
Canopy Biomass LiDAR version 2.0 built by the UMass Boston, conception by the KU Leuven, and prototyped by RIT.
Field of View of the CBL LiDAR. | Scan Pattern Projected onto a 3D Sphere. | Scan Pattern Projected onto a 3D Sphere.
Experimental Sites: Harvard Forest, USA (42°30′N, 72°12′W) and mangrove forests in Palau (7°31′49″N, 134°33′53″E), representing temperate and tropical ecosystems. |  | 
Raw terrestrial LiDAR point clouds from Harvard Forest (left) and the mangrove forest of Palau (right). |  | 
We introduce a three-stage pipeline for efficient 3D point cloud annotation: Spherical Projection TLS point clouds are unwrapped into 2D spherical maps based on azimuth and elevation, capturing features like intensity, range, and surface normals. Hybrid Annotation A segmentation model is trained on a small labeled set, then refined through active learning (manual correction of uncertain areas) and semi-supervised learning (confident pseudo-labels). |  |  | 
Back Projection Final 2D segmentation maps are projected back to 3D to generate labeled point clouds. |  |  | 
Single-Channel Spherical Feature Maps | Pseudo-RGB Spherical Map via Feature Stacking | Spherical Visualization of the 3D Scene | 
IV. Scene Semantic Segmentation | V. Individual Tree Isolation
VI. Tree Reconstruction | 
2D Segmentation (Unet++) Metrics: oAcc = 0.874, mAcc = 0.749, mIoU = 0.610. | 3D Segmentation (PointNet++) Metrics: oAcc = 0.935, mAcc = 0.906, mIoU = 0.834.
✅ Highlights Efficient Annotation Pipeline: Spherical projection + 2D models = faster, high-quality 3D labeling. Strong 2D Segmentation: Achieved ~90% accuracy; models generalized well across forest scenes and accelerated label refinement. Robust 3D Segmentation: PointNet++ reached 92–96% accuracy, though fine structures (e.g., roots, small objects) remain challenging. | 🔍 Future work Incorporate richer features for 3D Seg-model training. Improve tree isolation and tree reconstruction.
Pseudo-RGB feature map
Ground Truth
Pred
Mask
Confusion matrix on an example dataset
A Glimpse Through the Laser’s Eye
Imagine walking through a forest deep, Where roots entwine and branches sweep. Not just a picture, not just a glance, But a world preserved in a digital dance.
With LiDAR’s gaze, the trees stand tall, Their forms captured, trunk and all. No rustling leaves, no shifting light, Yet their silent shapes still hold the sight.
Step in, reach out, and feel the space, Where science and nature meet face to face. A glimpse of forests, mapped and true— A story of the wild, revealed to you.